## Slide 1
IT SYSTEMS SUPPORT · POWER FUNDAMENTALS
How a PSU Works
From the wall socket to every component — including a deep dive on the Rectifier and MOSFET.
MODULE
PSU & Power Delivery
REGION
South Africa (230 V AC)
LEVEL
Foundational — IT Support
AUDIENCE
Learners & Technicians
Investec · IT Systems Support · Learning content

## Slide 2
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
2
WHAT WE WILL COVER
The journey of electricity through your PC
Wall Outlet
230 V AC
PSU
Filter · Rectify · Regulate
Motherboard
Distribution
Components
CPU · GPU · Drives
Part 1 — Inside the PSU
8 steps from wall power to stable DC rails.
Part 2 — Where power goes
Motherboard, CPU, GPU, storage and fans.
Part 3 — Rectifier deep dive
AC → DC using diodes and a bridge rectifier.
Part 4 — MOSFET deep dive
The high-speed switch that makes it all work.

## Slide 3
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
3
PART 1
Inside the PSU
Eight steps that turn 230 V wall power into the clean, stable low-voltage DC every component needs.

## Slide 4
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
4
STEP 1
Power comes from the wall
Wall Outlet
230 V AC (South Africa)
Power Cable
Carries AC to the PC
Power Supply Unit
Where the magic happens
South African wall sockets provide 230 Volts AC (Alternating Current).
AC means the electricity constantly changes direction about 50 times every second (50 Hz).
Computer components cannot use AC power.
KEY POINT The wall gives us alternating current — but PCs can only run on direct current (DC).

## Slide 5
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
5
STEP 2
The PSU filters the electricity
The electricity first enters an EMI Filter.
Dirty Electricity
Noise · Spikes · Interference
EMI Filter
Cleans the incoming power
Clean Electricity
Safe for the next stage
Think of it like a water filter. It removes:
electrical noise
spikes
interference
KEY POINT Result: dirty electricity in, clean electricity out — like a water filter for power.

## Slide 6
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
6
STEP 3
AC becomes DC
Next comes the Rectifier.
230 V AC
Back and forth
Rectifier
One-way gate
320 V DC
One direction only
AC moves back and forth.
DC only moves one direction.
Computers only work on Direct Current (DC).
KEY POINT The rectifier converts 230 V AC into roughly 320 V DC — one direction only.

## Slide 7
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
7
STEP 4
High voltage is chopped into tiny pulses
The PSU uses high-speed transistors (MOSFETs).
Instead of using the electricity directly, it rapidly turns it ON / OFF / ON / OFF…
…about 50,000 – 500,000 times every second.
This creates high-frequency electricity.
Why? Because high frequency allows the transformer to be much smaller and more efficient.
MOSFET
Ultra-fast switch
ON / OFF Pulses
50 kHz – 500 kHz
Small Transformer
Efficient · Compact
KEY POINT Chopping DC into rapid pulses lets a tiny transformer do the work of a huge one.

## Slide 8
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
8
STEP 5
Transformer lowers the voltage
The transformer reduces the voltage. Example:
Transformer
+12 V
Motors & high power
+5 V
Electronics
+3.3 V
Chips & logic
KEY POINT Now we have the voltages a computer actually needs: +12 V, +5 V and +3.3 V.

## Slide 9
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
9
STEP 6
Output filters smooth everything
Capacitors remove tiny ripples.
Rough DC
Ripples remain
Capacitors
Absorb & release
Smooth DC
Stable output
This is extremely important.
The CPU needs very stable electricity.
Even tiny fluctuations can crash a computer.
KEY POINT Capacitors turn rippled DC into a rock-steady voltage that CPUs demand.

## Slide 10
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
10
STEP 7
Voltage regulators keep everything constant
Suppose your wall voltage changes. Instead of a wobbling output…
Without Regulation
12.0 V → 11.5 V → 12.7 V → 11.8 V → 12.3 V
With Regulation
12.00 V · 12.01 V · 11.99 V · 12.00 V
…the PSU constantly adjusts itself so the output stays almost perfectly stable.
KEY POINT The regulator watches the output non-stop and corrects it thousands of times per second.

## Slide 11
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
11
STEP 8
The PSU sends power to every component
Different components need different voltages.
PSU
Motherboard
CPU · RAM · Fans
GPU
Graphics card
Drives
SSD / HDD
KEY POINT The PSU is the central hub — every component ultimately gets its energy from here.

## Slide 12
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
12
PART 2
Where the power goes
Each rail (+12 V, +5 V, +3.3 V) feeds different components. Here is who uses what — and how.

## Slide 13
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
13
VOLTAGE RAILS · +12 V
The most powerful rail
The most powerful rail.
Used by: CPU, GPU, cooling fans, water pumps, motors in HDDs.
+12 V
CPU
GPU
Fans
HDD Motors
KEY POINT +12 V does the heavy lifting — CPUs, GPUs, fans and hard drive motors all pull from here.

## Slide 14
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
14
VOLTAGE RAILS · +5 V
Used for electronics
Used for electronics.
+5 V
SSD
HDD Logic Board
USB Devices
RGB Controllers
KEY POINT +5 V powers the digital electronics inside drives, USB ports and RGB.

## Slide 15
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
15
VOLTAGE RAILS · +3.3 V
Used by small chips
Used by small chips.
+3.3 V
RAM Electronics
Motherboard Chipset
BIOS Chip
PCIe Logic
KEY POINT +3.3 V feeds the low-power chips and logic that run RAM, chipset, BIOS and PCIe.

## Slide 16
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
16
DISTRIBUTION
How the motherboard distributes power
The motherboard receives power from the PSU and acts like a power distribution board.
PSU
+12 V · +5 V · +3.3 V
Motherboard
Power distribution board
Motherboard
CPU
RAM
Chipset
PCIe Slots
USB Ports

## Slide 17
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
17
CPU POWER IS SPECIAL
The motherboard steps 12 V down for the CPU
Although the PSU sends 12 V, the CPU cannot use 12 V directly.
Modern CPUs usually need about 0.8 V, 1.0 V, 1.1 V or 1.2 V.
So the motherboard contains VRMs (Voltage Regulator Modules).
The VRM acts like a precision power converter.
PSU
12 V
VRM
Precision converter
CPU
~1.1 V
KEY POINT The VRM converts 12 V from the PSU into the ~1.1 V the CPU actually runs on.

## Slide 18
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
18
GPU POWER
Graphics cards receive 12 V and regulate it internally
PSU
12 V
PCIe Cable
Dedicated GPU power
GPU
Internal regulators
Core · Memory · Controllers
Final destination
Graphics cards also receive 12 V.
Internal voltage regulators feed the GPU core, memory and controllers.
A high-end graphics card may consume 300–600 watts, so it has its own dedicated power connectors.
KEY POINT High-end GPUs pull hundreds of watts — they get their own PCIe power cables.

## Slide 19
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
19
SSD POWER
Very simple — one voltage only
PSU
5 V
SSD Controller
Flash memory
An SSD is much simpler. Very little power is needed.
KEY POINT SSDs have no motors — 5 V is enough for the controller and flash memory.

## Slide 20
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
20
HDD POWER
Hard drives need two voltages
12 V — Spins the platters
The motor uses 12 V
5 V — Runs the electronics
The controller chip uses 5 V
Hard drives need two voltages — one for the motor, one for the electronics.
KEY POINT Anything with a motor (HDD, fans, pumps) needs 12 V. Logic still runs on 5 V.

## Slide 21
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
21
FANS
Fans use 12 V
PSU
12 V
Motor
Converts current to rotation
Fan Spins
Cooling airflow
The motherboard can change the voltage or use PWM signals to control fan speed.
KEY POINT Fan speed is controlled by adjusting the voltage or using PWM signals.

## Slide 22
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
22
SUMMARY
The complete power journey
Wall Outlet — 230 V AC
EMI Filter
Rectifier (AC → DC)
High-Speed Switching (MOSFETs)
Transformer (steps down)
Rectifiers
Capacitors (smoothing)
Voltage Regulators
+12 V · +5 V · +3.3 V
Motherboard · GPU · SSD · HDD · Fans · USB

## Slide 23
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
23
SIMPLE ANALOGY
Imagine your house has a water treatment plant
Wall outlet
A large river
PSU
Cleans & controls water
Pipes
PSU cables
Motherboard
City water network
Buildings
CPU · GPU · SSD · RAM
The PSU makes sure every component gets exactly the right amount of clean, stable power. Too much power could damage the component, too little power could cause crashes, so the PSU continuously regulates and distributes electricity safely throughout the computer.
KEY POINT PSU = water treatment plant · Cables = pipes · Motherboard = city network · Components = buildings.

## Slide 24
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
24
PART 3
Rectifier deep dive
The one-way gate for electricity — how diodes turn AC into DC.

## Slide 25
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
25
1. WHAT IS A RECTIFIER?
The one-way gate for electricity
A rectifier is like a one-way gate for electricity.
Electricity from your wall outlet moves forward and backward (AC).
A rectifier only allows electricity to move forward, turning it into DC.
Think of it like a revolving door at a stadium.
AC
People walking in and out
Rectifier
Security lets people through one way
DC
Everyone walking the same way

## Slide 26
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
26
BEFORE THE RECTIFIER (AC)
Electricity keeps changing direction
→ ← → ← → ←
AC current flow
Sine Waveform
Positive then negative
Voltage: /\ /\
/ \ / \
___________/ \____/ \___
\ /
\ /
\/
The voltage goes positive…
then negative…
50 times every second.

## Slide 27
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
27
AFTER THE RECTIFIER (DC)
Electricity only flows in one direction
→ → → → → →
One direction
Flat DC Waveform
Steady, forward only
────────────────────────────────
Now the computer can use it.

## Slide 28
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
28
HOW DOES A RECTIFIER WORK?
Diodes — one-way valves for electricity
Inside are special electronic parts called diodes.
A diode behaves like a one-way valve — forward is allowed, backward is blocked.
A PSU usually uses four diodes arranged in a Bridge Rectifier.
This converts 230 V AC into approximately 320 V DC.
Forward
Allowed
Diode
One-way valve
Backward
Blocked
Bridge Rectifier
Four diodes together
KEY POINT Four diodes wired as a bridge convert 230 V AC into ~320 V DC.

## Slide 29
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
29
WHERE IS THE RECTIFIER INSIDE THE PSU?
Location in the power chain
Wall Outlet
EMI Filter
Rectifier You are here
MOSFETs
KEY POINT The rectifier sits after the EMI filter and before the high-speed MOSFET switches.

## Slide 30
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
30
PART 4
MOSFET deep dive
The impossibly-fast electronic switch that makes the modern PSU possible.

## Slide 31
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
31
2. WHAT ARE MOSFETS?
Metal-Oxide-Semiconductor Field-Effect Transistor
MOSFET stands for: Metal-Oxide-Semiconductor Field-Effect Transistor
That sounds complicated, but its job is actually simple.
MOSFET
A transistor
Electronic Switch
ON / OFF at incredible speed

## Slide 32
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
32
MOSFET · SIMPLE EXPLANATION
An extremely fast electronic switch
A MOSFET is an extremely fast electronic switch.
Imagine someone turning a light switch on and off: ON / OFF / ON / OFF.
A human can do this maybe once every second.
Human
≈ 1 switch per second
MOSFET
100,000 · 200,000 · 300,000 · 500,000 times every second
KEY POINT A MOSFET can switch hundreds of thousands of times per second — far beyond human speed.

## Slide 33
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
33
WHY SWITCH SO FAST?
Because it makes the transformer tiny and efficient
The PSU needs to reduce the voltage. Instead of using a huge transformer like older power supplies, modern PSUs:
1. Convert
AC to DC
2. Chop
DC into tiny pulses
3. Send
Pulses through a small transformer
This makes the PSU:
much smaller
much lighter
more efficient
cooler

## Slide 34
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
34
MOSFET WAVEFORM
Instead of a smooth wave — tiny square pulses
Instead of a smooth wave…
──────────────────────────────
…the MOSFET creates tiny square pulses:
_|‾|_|‾|_|‾|_|‾|_|‾|_|‾|_|‾|_|‾|_
These pulses can be over 100,000 times per second.
KEY POINT MOSFETs replace smooth waves with rapid square pulses — the language of switching PSUs.

## Slide 35
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
35
WHY NOT LEAVE THE ELECTRICITY ON?
The swimming-pool analogy
Filling a Pool
Instead of one huge bucket…
Many Tiny Cups
Poured very quickly
Easier to Control
Exactly what a MOSFET does
Imagine filling a swimming pool.
Instead of one huge bucket… you pour many tiny cups very quickly.
It becomes much easier to control.
That's exactly what a MOSFET does with electricity.

## Slide 36
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
36
WHAT HAPPENS AFTER THE MOSFET?
It enables the transformer to do its job
Wall Outlet
Rectifier
MOSFET You are here
Transformer
Low Voltage
KEY POINT The transformer only works because the MOSFET is switching so rapidly.

## Slide 37
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
37
WHY ARE MOSFETS SO IMPORTANT?
They power the modern electronic world
Without them the PSU would be:
much bigger
heavier
less efficient
hotter
more expensive
Nearly every modern electronic device uses MOSFETs, including:
Computer PSUs
Motherboards
Graphics cards
Laptop chargers
Phone chargers
Electric vehicles
Solar inverters

## Slide 38
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
38
RECTIFIER VS MOSFET
Side-by-side comparison
Aspect | Rectifier | MOSFET
Job | Converts AC to DC | Switches DC on and off at very high speed
Built from | Diodes | Transistors
Controls | Only the direction of current | When current flows
Stage in PSU | First major conversion stage | Second major conversion stage
Produces | DC power | High-frequency pulses
KEY POINT Rectifier = converts AC into DC. MOSFET = switches DC on and off very fast.

## Slide 39
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
39
THE COMPLETE PSU PROCESS
End-to-end from wall power to your components
230 V AC Wall Power
EMI Filter Removes noise
Bridge Rectifier AC → DC
320 V DC
MOSFETs Fast electronic switches
High-Frequency Pulses
Transformer Steps voltage down
Rectifiers & Filters
Stable +12 V, +5 V, +3.3 V DC
Motherboard · CPU · GPU · RAM · SSD · Fans

## Slide 40
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
40
A GOOD WAY TO REMEMBER THEM
Two simple pictures
Rectifier = Translator
Changes the type of electricity from AC to DC.
MOSFET = Super-fast switch
Chops that DC into high-frequency pulses so the transformer can efficiently produce the different voltages your PC components need.
KEY POINT Rectifier = translator (AC → DC). MOSFET = super-fast switch (chops DC into pulses).

## Slide 41
How a PSU Works · Rectifier & MOSFET Deep Dive · IT Systems Support
41
You now understand how a PSU works.
From 230 V AC at the wall, through filtering, rectification, MOSFET switching, transformation, smoothing and regulation — to the exact voltages every component needs.
Investec · IT Systems Support · Power Fundamentals